## Slide 1: SWP Operations Overview
Central Coast Water AUTHORITY
Oct 24, 2024

## Slide 2: Outline
CA hydrology
SWP system
Regulations
SWP Allocations
SWP Outlook

## Slide 3: Hydrology

## Slide 4: Majority of Runoff in the Northern California

## Slide 5: California Has High Precipitation Variability When Compared with Rest of Continental U.S.
https://escholarship.org/uc/item/2r71j15r

## Slide 6: Uncertain and Variable Interannual HydrologY
Notes: For Northern Sierra 8-Station:
https://cdec.water.ca.gov/prev_barcharts8SI.html

## Slide 7
SWP Source Watersheds

## Slide 8
Typical Source of SWP Exports in November to May

## Slide 9
Typical Source of SWP Exports in June to October

## Slide 10: Historic and Future Runoff Patterns
Climate Change Creates Challenges to Future Reservoir Operations

## Slide 11
Stairstep pattern in WY 2022 exemplifies new extremes and variability associated with climate change
Wet
Dry
Wet
Wet
Dry
Dry

## Slide 12
Stairstep pattern continued in WY 2023, even though completely different hydrology
Wet
Dry
Wet
Wet
Dry
Dry

## Slide 13: SWP Facilities

## Slide 14
State Water Project
34 storage facilities, reservoirs and lakes
20 pumping plants
4 pumping-generating plants
5 hydroelectric power plants
701 miles of open canals and pipelines
Construction began in the 1960s

## Slide 15
Key SWP Facilities Built to Capture Water Under Historic Runoff Patterns

## Slide 17
SWP Service Areas

## Slide 18: SWP Regulations

## Slide 19: Regulatory Limits for SWP and CVP
SWP Water Right Permits
Bay Delta Water Quality Control Plan (D-1641)
ESA Biological Opinions (BiOps)
CESA Permit
SWP Diversions to Storage and for Exports
CVP Water Right Permits
Bay Delta Water Quality Control Plan (D-1641)
ESA Biological Opinions (BiOps)
CVP Diversions to Storage and for Exports

## Slide 20: State Water Board’s Bay-Delta Water Quality Control Plan (WQCP)

## Slide 21: Status of Fish Species Resulted in Additional Regulatory Restrictions

## Slide 22: CVP and SWP Permits Updated Periodically
BiOps
WQCP (D1641)
BiOps and CESA permits
BiOps and CESA ITP
Interim Operations Plan (IOP)
New BiOps & ITP
New WQCP (VAs)
Interim Operations Plan (IOP)
Protect ESA listed species: Winter-run, Spring-run, Steelhead, Green Sturgeon, Delta Smelt and Longfin smelt*
Protect CESA listed species: Winter-run, Spring-run, Delta Smelt, Longfin smelt and White Sturgeon*
(Flows and Export limits)
Protects beneficial uses in the Delta (flows, salinity, export limits)
1995
2004
2008-09
2019-20
2022
2023-24
2024-25

## Slide 23
Chipps Island
N
Port Chicago
64
85
81
Outflow
Pacific Ocean
X2 locations
75
95
Collinsville
Emmaton
Threemile Slough
West False River Drought Barrier
Jersey Point
Delta Cross Channel Gates
Rock Slough
Rio Vista
State Water Board Bay-Delta Standards (Decision-1641)
  Delta Flow and Outflow requirements
  Salinity requirements
  Export limits
ESA Biological Opinions
  Old and Middle River Flow Requirements
  Export limits
  Delta outflow requirements
CESA Incidental Take Permit
  Export limits
  Delta outflow requirements
Bay – Delta Regulations

## Slide 24
OMR Requirements:
  Limit net reverse flows in Old and Middle Rivers
  Limit how much flow comes from the north and central Delta to south Delta
Therefore, south Delta exports depend on the San Joaquin River flow
For the same OMR Requirement, higher south Delta exports with higher San Joaquin River flow and vice-versa
Old and Middle River Flow (OMR) Requirements

## Slide 25: SWP Allocations

## Slide 26: SWP Annual Allocation Process
OCT
NOV
DEC
JAN
FEB
MAR
APR
MAY
JUN
JUL
AUG
SEP
(30/50/60/100% Delivery Schedules Due)
SWP Studies
(Initial Allocation Announced)
(Prior-Year Finalizations Due)
Prior Year Finalizations
(Begin SWP Water Year)
- Schedule Updates and Monthly Status Reports
(Typical Final Allocation Announced)

## Slide 27: SWP Allocation Process
Update SWP Water Operations Annual Plan Allocation: Revise, as needed
Storage Conditions
Forecasted Hydrology
Actual/Forecasted Demands
Real-time Operations
Next Month
State/Federal
Environmental Requirements

## Slide 28: SWP Allocation Process
Update SWP Water Operations Annual Plan Allocation: Revise, as needed
Storage Conditions
Forecasted Hydrology
Actual/Forecasted Demands
Real-time Operations
Next Month
State/Federal
Environmental Requirements

## Slide 29: Hydrology Forecast
Forecast Availability
Nov
  Historical Exceedance
Dec – Jan
  DFM forecast (precipitation)
Feb – May
  DFM forecast (incorporates snow)
Notes: Initially based on historic exceedances
Starting in Dec
  Suite of hydro from DFM
  First 2 are based on precip
  Starting feb incorporate snow

## Slide 30: Observations and Forecasts Informing Water Management
AR Recon

## Slide 31: Regulations & Obligations
Minimum Instream flow
Flood control
Delta requirements
  State Water Board Bay-Delta Standards (Decision-1641)
  ESA Biological Opinions
  CESA Incidental Take Permit
Other In-Basin Use
Coordinated Operations Agreement
Notes: Initially based on historic exceedances
Starting in Dec
  Suite of hydro from DFM
  First 2 are based on precip
  Starting feb incorporate snow

## Slide 32: Storage Operational Goals
Carryover Targets
  Oroville
    1.6 MAF end of September
  San Luis
    State Water Contractors Carryover
    San Luis Low Point
Terminal reservoir seasonal operations

## Slide 33: Deliveries Forecasts
Range of delivery requests
  0%, 10%, 30%, 50%, 60%, 100%
Table A scaled to maximize delivery of available supply
Other Deliveries (not scaled)
  Article 56
  Backup

## Slide 34
Chart: Historic Initial and Final SWP Table A Allocations
| 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
Final Allocation | 100 | 100 | 100 | 100 | 90 | 39 | 70 | 90 | 65 | 90 | 100 | 60 | 35 | 40 | 50 | 80 | 65 | 35 | 5 | 20 | 60 | 85 | 35 | 75 | 20 | 5 | 5 | 100 | 40
Initial Allocation | 75 | 70 | 40 | 55 | 50 | 40 | 20 | 20 | 35 | 40 | 55 | 60 | 25 | 15 | 5 | 25 | 60 | 30 | 5 | 10 | 10 | 20 | 15 | 10 | 10 | 10 | 0 | 5 | 10

## Slide 35: Complex Water Management: WY 2022 Example
Time
Oct
Dec
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Nov
Initial
Allocation
Allocation Revisions
Obtain Initial Demands
AR5
Heat
Dome
Record Dryness
Warm
And
Dry
Dry Season/
Monsoon
2019 BiOp Lawsuit & IOP
WIND
TS Kay
Final
Allocation
TUCO
0% + HH&S
20%
5% + HH&S
TUCP
TUCP
TUCP Withdrawn
Notes: Here is a graphic illustrating the seasonal perspective of water management below the timeline and the way water year 2022 played out above the timeline. Fall rains started on time with the record-setting atmospheric river in late October. However, November was warm and dry that began to dry out the landscape again before December kicked in with abundant precipitation and snowfall. The seasonal snowpack got off to a great start, but the new calendar year brought a new record setting stretch of warm and dry limiting further growth and further easing of drought conditions. By April 1 the snowpack was very limited but spring rains helped the snowmelt make it to the streams and rivers. The summer brought more heat and some new extremes with the Southwest Monsoon including flooding in Death Valley National Park in August. In September a record-setting heat wave took place and was disrupted by a decaying Pacific hurricane which was still a tropical storm when it impacted southern CA. Shortly after that a decayed typhoon impacted northern California as a cutoff low that spun offshore. While the timing of events helped, the pace and scale were off leading to the continuation of the drought. In fact, 2020-2022 is now the driest three-year stretch for statewide water-year precipitation breaking the previous record set in 2013-2015.

## Slide 36: SWP Outlook

## Slide 37
Source: 2019 BiOps from DWR’s LTO EIR PP model. 2020 ITP results estimated using DWR’s LTO EIR Alt2B model. VA results estimated using DWR’s LTO EIR PP model. 55% UIF results based on Nov 2019 SWRCB models. Note that models do not include potential real time export restrictions.
Relationship of VA to BiOps, ITP and WQCP
Estimated changes in Banks PP exports compared to 2008-09 BiOps
VA modeling reflects initial water user VA proposal
Compared to 2008-09 BiOps:
If ITP outflow elements are replaced by VA, 2019 BiOps improvements largely continue
55% UIF likely results in significant reductions in SWP exports
VA flows will address ESA and CESA spring outflow requirements

## Slide 38: Resultant Water Supply Comparison

## Slide 39: Decreasing Trend in SWP Allocations
Chart: 
| 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043
Final Allocation | 1 | 1 | 1 | 1 | 1 | 0.9 | 0.39 | 0.7 | 0.9 | 0.65 | 0.9 | 1 | 0.6 | 0.35 | 0.4 | 0.5 | 0.8 | 0.65 | 0.35 | 0.05 | 0.2 | 0.6 | 0.85 | 0.35 | 0.75 | 0.2 | 0.05 | 0.05 | 1 | 0.4
Long Term Reliability | 0.77 | 0.77 | 0.77 | 0.77 | 0.77 | 0.77 | 0.77 | 0.77 | 0.77 | 0.77 | 0.77 | 0.77 | 0.77 | 0.675 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.58 | 0.58 | 0.56 | 0.56 | 0.53
Future Reliability (Lower) | 0.53 | 0.524 | 0.518 | 0.512 | 0.506 | 0.5 | 0.494 | 0.488 | 0.482 | 0.476 | 0.47 | 0.464 | 0.458 | 0.452 | 0.446 | 0.44 | 0.434 | 0.428 | 0.422 | 0.416 | 0.41
Future Reliability (Higher) | 0.53 | 0.5265 | 0.523 | 0.5195 | 0.516 | 0.5125 | 0.509 | 0.5055 | 0.502 | 0.4985 | 0.495 | 0.4915 | 0.488 | 0.4845 | 0.481 | 0.4775 | 0.474 | 0.4705 | 0.467 | 0.4635 | 0.46

## Slide 40: What is the Delta Conveyance Project (DCP)?
DWR issued FEIR/NOD in 12/2023 and selected Bethany Reservoir Alignment
Two new diversion intakes in the north Delta with state-of-the-art fish screens
Total diversion capacity of 6,000 cfs (3,000 cfs each)
45 miles of 36-feet single tunnel, from new intakes to California Aqueduct at Bethany Reservoir
New pumping plant connecting the tunnel to Bethany Reservoir

## Slide 41: Questions?

## Slide 42: SWP Water Supply Allocation Inputs
Oroville
Storage
Forecasted Dry Hydrology
- Inflow to Reservoirs
- Runoff to Bay-Delta
South of Delta Storage San Luis Reservoir
SWP Actual and Forecasted Contractor Demands
Releases
Export
Deliveries
Central Valley Project (CVP) Operations
BiOps/ITP
Bay-Delta Regulatory Objectives
Delta Outflow
Water Quality
Delta
Notes: Pull in data from a variety of sources
  Suite of Hydro from DFM (Seans group)
    Estimates inflows/runoff
    Informs potential regulatory requirements
  CVP operation from Reclamation
  Storage
  Demands from SWC and processed by mahmouds group
Strategy
  Simulate the project operations
  Winter/spring
    Minimize releases – build storage
    Maximize export of un-stored water
  Summer
    Manage Oroville storage to requirements
    Export Available storage
  Scale TA deliveries to maximize delivery
    Resulting TA is what is used to determine allocation percentage